TECHNICAL SPECIFICATION FOR Type TP - TELESCOPIC & FIXED SEATING

The seating layout to meet the requirements of BSEN 13200-1 [layout criteria]

TELESCOPIC PLATFORMS

DESIGN LOADS

In addition to its own weight the structure to be designed to withstand;

Floor loading:	5kN/Sq.Metre   [104 lbs per sq. ft.]

Horizontal Sway:	7.5%

Max deflection:	1/200 at Design Load.

Side safety rails :	1kN/Metre UDL at 1.1m high. (Adjacent to seats)  [68.3 lbs/ft at 3.61 ft high]

Side safety rails :	1.5kN/Metre UDL at 1.1m high. (Adjacent to aisle)  [102.4 lbs/ft at 3.61 ft high]

The seating system to meet the requirements of;

ICC 300-2007 Telescopic Seating.

BS EN 13200 - 5 Telescopic Stands.

BS 6399 (where applicable)

EN 12727 Seat Testing Methods (Grade 4).

MAIN PLATFORM

Each main platform assembly (row) to be a lightweight, welded steel space-frame that provides strength, stiffness and accuracy to the whole system. Note systems with bolted together platforms will Not be acceptable. Each platform assembly is constructed from steel tubes and steel pressings of the following sizes;

Front Beam	76 x 76 x 30 x 2mm [3” x 3” x 1.18” x 0.8”]  S275 Pressed Steel Beam.

Rear Beam	195 x 45 x 2.5mm [7.68” x 1.77” x 0.1”]   S275 Pressed Steel Beam.

Supports	50 x 40 x 12.5 x 2 mm [2” x 1.57” x 0.5” x 0.8”]  S275 Pressed Steel ‘Top Hat’ Section.

Other Parts	Pressed steel, profiled sections of minimum thickness 3mm.

Finish	Cleaned, de-greased and epoxy powder coated, baked at 180C.

Standard colours: RAL 9005 Satin Black.

Deck (floor)	19mm [0.75”] thick, tongued and grooved, Spruce plywood, bonded to Class 3, BS EN314:1993, listed in BS 5268, Part 2, Section 4 for structural building use and orientated for grain to run front to back on platform space-frame for extra stiffness. Carpet:	Ref: Rawson ‘Eurocord’, to client colour choice.

MAIN COLUMNS

Each column is a welded sub-frame with an ‘adjustable cantilever arm’ for height adjustment of each row when installed. Systems without adjustable cantilevers will not be acceptable. There are 2 Main Columns per row of section structure. All columns to be fitted with automatic row latching at floor level and vertical restraints at high level.

Each column foot has 4 wheels installed, giving 8 per row in contact with the floor per row of section.

Wheels:	125mm [5”] diameter x 40mm  [1.57”]  width c/w nylon hub, polyurethane tyre & roller bearing. Note smaller wheels will not be acceptable.

Column:	100 x 50 x 3.2mm  [4” x 2” x 0.126”]  steel, Rolled Hollow Section.  (Stiffened on Rows 10 to 15 with a secondary 50 x 50 x 3mm  [2” x 2” x 0.12”]  steel Rolled Hollow Section, and 100 x 50mm  [4” x 2”]   on rows 16 to 19)

Column Foot:	90 x 50 x 3mm  [3.54” x 2” x 0.12”]  S275 Steel Pressed Channel.

Finish:		Cleaned, de-greased and epoxy powder coated, baked at 180C.

Standard colours: RAL 9005 Satin Black.

COLUMN BRACES

Each vertical column is braced diagonally with a bolted brace member connecting column to main platform assembly.

Brace:		40 x 40 x 3mm  [1.57” x 1.57” x 0.12”]  Steel Angle. (Rows 1 – 5)

Brace:		50 x 50 x 2.5mm  [2” x 2” x 0.1”]  Steel R.H.S. (Rows 6 upwards)

PLATFORM GUIDANCE

Each row is to be aligned by Parallel Guidance Frames working on the ‘scissor’ principle to prevent jamming and ensure accurate opening and closing of the telescopic platform.

Guide Arms	40 x 40 x 3mm  [1.57” x 1.57” x 0.12”]  steel angle.

Cross Tube	25 x 25 x 3mm  [1” x 1” x 0.12”]  steel R.H.S.

ROW TO ROW CONTACT

Each row of platforms to transfer load to the row below through moulded nylon Load Transfer Skids, to reduce noise and reduce friction during opening and closing operation.

ROW TO ROW LOCKING

Each main column to lock on opening automatically through gravity action latch locks. These also prevent accidental closing and allow partial opening of rows.

INTERMEDIATE STEPS

Each spectator aisle is fitted with intermediate half-steps, each 1100mm wide and ½ row rise high to ensure safe and easy access up and down the aisle.

Step:	2mm  [0.08”]  S275 Steel Pressing c/w full width extruded aluminium, non-slip nosing fixed to front edge c/w integral photo luminescent strips.

Step Frame	2mm  [0.08”]  thick pressed steel, epoxy powder coated finish.

SAFETY RAILS

The ends of each seating block row are fitted with a re-moveable safety rail. Each section is re-moved before closing the seating. The rail system to withstand a UDL of 1kN/metre.

Rail:		50 x 20 x 2mm  [2” x 0.79” x 0.08”]  oval shaped steel top tube.

Uprights:	30 x 30 x 2.5mm  [1.18” x 1.18” x 0.1”]  square steel tube.

Infill:	Vertical steel tubular members at <100mm  [4”]  spacing. 19 x 19 x 1.6mm  [0.75” x 0.75” x 0.063”]  Sq. ERW tube

Or

Panels with laminate finish, laminate to be chosen from the Kronospan range.

Or

Acrylic panels,  tinted grey

Finish:		Cleaned, iron phosphate pre-treatment and epoxy powder to colour choice.

FRONT FASCIAS

Front fascias to be fitted to the front of each platform to create a closed in, panelled effect when the seating platforms are closed.

Fascias	15mm  [0.6”]  thick MDF with laminate finish and edges capped. Laminate to be chosen from the Kronospan range.

ROW 1 FASCIA

Kick Panel:	2.5mm  [0.1”]  S275 Steel Profiled full length panel

Finish:		Cleaned, iron phosphate pre-treatment and epoxy powder to colour choice.

SYSTEM OPERATION

Power Operation

End safety rails to be fitted and removed manually.

Power Operation Unit

Electrical power operation drive units to be fitted under each Row 1 platform assembly.

The system is by the ‘friction drive’ method, driving onto the hall floor with 4 No. vulcanised rubber covered, cast iron drive rollers per unit. There is generally one power unit per telescopic platform

module.

Drive Roller:	150 [6”] dia. x 100 [4”] long  (4 driving thro 2 No. drive shafts)

Motor:		3 ph, 240v, 60Hz, 0.5Hp, 1.25 SF, 1425 rpm.

Gearbox:	Output Ratio = 87:1.

The drive rollers are chain driven and so adjustment mechanisms are provided on drive shaft bearings to re-tension chains (if required). The adjustment mechanisms on the opposite side of the power unit are to provide adjustment of tracking on telescopic platform, when extending and retracting.

These units are contained safely within the understructure and require no supervision or maintenance apart from a greasing of the drive chains and bearings and a checking of chain tension during the routine annual maintenance contract.

Control Panel

The power operation units are run from a control panel mounted on the wall behind the telescopic platform. The switch gearing for the motors is provided by a Frequency Inverter, which is rated to suit the number of electric motors being controlled. The inverter converts the supply to suit the motors, which means that the power supply to the seating unit is;

Power supply rating: Single Phase (1ph), 120v, 60Hz. Current rating dependant on project.

This system provides thermal motor protection, along with variable parameters such as;

Operating speed.

Acceleration

Deceleration.

Note: Having a gradual acceleration reduces wear on the drive unit, the seating structure and decreases the required starting torque.

The control panel is IP65 rated with a door interlocking power isolating switch.

Control Pendant

A clearly labelled, low voltage pendant control to be supplied to control the motor drive system.

(To extend or retract the telescopic platform units firstly unscrew the sealing cap on the electrical socket mounted centrally on the low kickboards. Then screw into place the electrical plug of the control pendant.)

The pendant to be supplied with just two arrow marked buttons. Depressing one or the other will slowly start the motors to extend or retract the telescopic platform units. While the motors are in operation an audible warning sounder mounted on the control panel to function.

The control wiring for the control pendant is low voltage dc.

CHAIR SYSTEMS

Type 	‘GALLERY 2 PC - SS150’ folddown fully upholstered chairs with armrests, grouped in 3 and 4 seat units and manually folded down onto platforms. The folding mechanism to be ‘foot operated for unlocking the chairs and to automatically lock when the chair is returned to the upright position for use.

Chair Frame	Welded tubular and pressed steel, beam mounted design.

Beam	50 x 50 x 2mm  [2” x 2” x 0.08”]  Square, steel tube.

Tip mechanism	Near silent, injection moulded plastic c/w neoprene ‘up’ and ‘down’ stops.

The spring activated stop mechanism will be fully enclosed so it cannot trap fingers or clothing. (Safe for small children).

Gas Struts	Dual action gas struts to be incorporated to assist the lifting of the assembly and control the descent speed.

Seat & Back	To be laminated, 12mm  [0.47”]  thick, pre-formed plywood construction, contoured with 35 CMFR [ Backrest] and 50 CMFR [Seat pan] fabricated foam to suit FR Code BS 5852 pt2 (Crib 5)and upholstered with fabric to spec and colour choice

Armrests:	Moulded plastic.

Finish	Metalwork, iron phosphate pre-treatment + epoxy powder coating, Standard colour RAL 9005 Satin Black Texture

Size	See layout drawings

Type: 	‘ARTS PC - SS140’ Front beam mounted, fully upholstered Theatre Chair c/w ABS contoured armrests. Mounted in groups of 2, 3 and 4 seats The backrest only to manually fold down backwards onto telescopic platforms.

When occupied the folding mechanism must tighten or ‘lock up’ when downwards vertical load is applied to the armrests.

Chair Frame:	Welded tubular and pressed steel, beam mounted design.

Tip mechanism:	Near silent, injection moulded reinforced nylon fully enclosed body c/w neoprene ‘up’ and ‘down’ stops.

The spring activated stop mechanism is to be fully enclosed so it cannot trap fingers or clothing. (Safe for small children).

Seat & Back:	To be laminated, 12mm  [0.47”]  thick, pre-formed plywood construction, contoured with 35 CMFR [ Backrest] and 50 CMFR [Seat pan] fabricated foam to suit FR Code BS 5852 pt2 (Crib 5)and upholstered with fabric to spec and colour choice.

Seat assembly to be removed easily (30 seconds) for maintenance.

Armrests:	Moulded plastic.

Finish:	Metalwork, iron phosphate pre-treatment + epoxy powder coating, Standard colour RAL 9005 Satin Black Texture

Fabric: Bradbury ‘Flamblend’ to client colour choice.

Seat Crs:	500mm nominal and subject to site survey.

Type 	‘METRO BY HSW’ folddown padded chairs with armrests, grouped in 3 and 4 seat units and manually folded down onto platforms. The folding mechanism to be ‘foot operated for unlocking the chairs and to automatically lock when the chair is returned to the upright position for use.

Armrests:	Moulded plastic, with automatic setting / striking feature.  Manual armrests will not be acceptable.

All armrests to be shared for aesthetic reasons, plus the requirement to maximise the seat centre, double armrests where chair banks meet will not be acceptable.

Seat Numbers	Included

Key Requirements : -

- Seat Pan hinge mechanism / up and down stops must be fully concealed to prevent any possibility of finger traps for health and safety reasons.  Chairs with exposed hinge mechanisms or up/down stops will not be acceptable.

- Underside of seat pan and rear surface of backrest must be plastic for durability reasons.

- Upholstery to the top surface of the seat pan and front face of the backrest.

- For long term flexibility chairs to be ‘rail based’ so the seating can be easily  re-configured by the client at any point in the life time of the installation if required. Chairs that cannot be reconfigured will Not be acceptable.

- Writing tablets to have integral ‘Anti Panic’ system to ensure the tablet moves to the shut position when the chair is vacated. Chairs without this feature are Not acceptable

Upholstered Benches and Backrests

Bench	Upholstered Bench incorporating front fascia with laminate finish.  Laminate to be chosen from the Kronospan range.

Backrest	Upholstered Backrest in a steel frame.   Note  upholstered backrest, without a steel frame to protect all the edges, will not be acceptable for durability reasons..

Fabric	Flamblend range by Bradbury Fabrics or similar.

CONTACT

Hussey Seatway Ltd.,

3 Centurion Way

Crusader Park

Warminster

Wiltshire     BA12 8BT

Tel:	01985 847200

Fax:	01985 847300

E-mail:	info@husseyseatway.com